## Slide 2: Overview
Iterative combinational circuits
Binary adders
  Half and full adders
  Ripple carry and carry lookahead adders
Binary subtraction
Binary adder-subtractors
  Signed binary numbers
  Signed binary addition and subtraction
  Overflow
Binary multiplication
Other arithmetic functions
  Design by contraction

## Slide 3: Iterative Combinational Circuits
Arithmetic functions
  Operate on binary vectors
  Use the same subfunction in each bit position
Can design functional block for subfunction and repeat to obtain functional block for overall function
Cell - subfunction block
Iterative array - a array of interconnected cells
An iterative array can be in a single dimension (1D) or multiple dimensions

## Slide 4: Block Diagram of a 1D Iterative Array
Example: n = 32
  Number of inputs = ?
  Truth table rows = ?
  Equations with up to ? input variables
  Equations with huge number of terms
  Design impractical!
Iterative array takes advantage of the regularity to make design feasible
Notes: Number of Inputs = 66
Truth Table Rows = 266
Equations with up to 66 variables

## Slide 5: Functional Blocks: Addition
Binary addition used frequently
Addition Development:
  Half-Adder (HA), a 2-input bit-wise addition functional block,
  Full-Adder (FA), a 3-input bit-wise addition functional block,
  Ripple Carry Adder, an iterative array to perform binary addition, and
  Carry-Look-Ahead Adder (CLA), a hierarchical structure to improve performance.

## Slide 6: Functional Block: Half-Adder
A 2-input, 1-bit width binary adder that performs the following computations:
A half adder adds two bits to produce a two-bit sum
The sum is expressed as a sum bit , S and a carry bit, C
The half adder can be specified as a truth table for S and C 
X
0
0
1
1
+ Y
+ 0
+ 1
+ 0
+ 1
C S
0 0
0 1
0 1
1 0
X
Y
C
S
0
0
0
0
0
1
0
1
1
0
0
1
1
1
1
0

## Slide 7: Logic Simplification: Half-Adder
The K-Map for S, C is:
This is a pretty trivial map! By inspection:
and
These equations lead to several implementations.
Y
X
0
1
3
2
1
1
S
Y
X
0
1
3
2
1
C
)
Y
X
(
)
Y
X
(
S
Y
X
Y
X
Y
X
S
+
×
+
=
Å
=
×
+
×
=
)
(
C
Y
X
C
)
Y
X
(
×
=
×
=

## Slide 8: Five Implementations: Half-Adder
We can derive following sets of equations for a half-adder:
(a), (b), and (e) are SOP, POS, and XOR implementations for S.
In (c), the C function is used as a term in the AND-NOR implementation of S, and in (d), the function is used in a POS term for S.
Y
X
C
)
(
S
)
c
(
Y
X
C
)
Y
X
(
)
Y
X
(
S
)
b
(
Y
X
C
Y
X
Y
X
S
)
a
(
Y
X
C
×
=
=
×
=
+
×
+
=
×
=
×
+
×
=
×
+
Y
X
C
Y
X
S
)
e
(
)
Y
X
(
C
C
)
Y
X
(
S
)
d
(
×
=
Å
=
+
=
×
+
=
C

## Slide 9: Implementations: Half-Adder
The most common half adder implementation is: (e)
A NAND only implementation is:
Y
X
C
Y
X
S
×
=
Å
=
)
(
C
C
)
Y
X
(
S
)
Y
X
(
×
=
×
+
=
X
Y
C
S
X
Y
C
S

## Slide 10: Functional Block: Full-Adder
A full adder is similar to a half adder, but includes a carry-in bit from lower stages. Like the half-adder, it computes a sum bit, S and a carry bit, C.
  For a carry-in (Z) of 0, it is the same as the half-adder:
  For a carry- in (Z) of 1:
Z
0
0
0
0
X
0
0
1
1
+ Y
+ 0
+ 1
+ 0
+ 1
C S
0
0
0 1
0 1
1 0
Z
1
1
1
1
X
0
0
1
1
+ Y
+ 0
+ 1
+ 0
+ 1
C S
0 1
1 0
1 0
1
1

## Slide 11: Logic Optimization: Full-Adder
Full-Adder Truth Table:
Full-Adder K-Map:
X
Y
Z
C
S
0
0
0
0
0
0
0
1
0
1
0
1
0
0
1
0
1
1
1
0
1
0
0
0
1
1
0
1
1
0
1
1
0
1
0
1
1
1
1
1
X
Y
Z
0
1
3
2
4
5
7
6
1
1
1
1
S
X
Y
Z
0
1
3
2
4
5
7
6
1
1
1
1
C

## Slide 12: Equations: Full-Adder
From the K-Map, we get:
The S function is the three-bit XOR function (Odd Function):
The Carry bit C is 1 if both X and Y are 1 (the sum is 2), or if the sum is 1 and a carry-in (Z) occurs. Thus C can be re-written as:
The term X·Y is carry generate.
The term XY is carry propagate.
Z
Y
Z
X
Y
X
C
Z
Y
X
Z
Y
X
Z
Y
X
Z
Y
X
S
+
+
=
+
+
+
=
Z
Y
X
S
Å
Å
=
Z
)
Y
X
(
Y
X
C
Å
+
=

## Slide 13: Implementation: Full Adder
Full Adder Schematic
Here X, Y, and Z, and C (from the previous pages) are A, B, Ci and Co, respectively. Also, G = generate and P = propagate.
Note: This is really a combination of a 3-bit odd function (for S)) and Carry logic (for Co): (G = Generate) OR (P =Propagate AND Ci = Carry In)
Co = G + P · Ci
Ai
Bi
Ci
Ci+1
Gi
Pi
Si

## Slide 14: Binary Adders
To add multiple operands, we “bundle” logical signals together into vectors and use functional blocks that operate on the vectors
Example: 4-bit ripple carry adder: Adds input vectors A(3:0) and B(3:0) to get a sum vector S(3:0)
Note: carry out of cell i becomes carry in of cell i + 1
Description
Subscript
3 2 1 0
Name
Carry In
0 1 1 0
Ci
Augend
1 0 1 1
Ai
Addend
0 0 1 1
Bi
Sum
1 1 1 0
Si
Carry out
0 0 1 1
Ci+1

## Slide 15: 4-bit Ripple-Carry Binary Adder
A four-bit Ripple Carry Adder made from four 1-bit Full Adders:

## Slide 16: Unsigned Subtraction
Algorithm:
  Subtract the subtrahend N from the minuend M
  If no end borrow occurs, then M ³ N, and the result is a non-negative number and correct.
  If an end borrow occurs, the N > M and the difference M - N + 2n is subtracted from 2n, and a minus sign is appended to the result.
Examples:
0 1 1001 0100 - 0111 - 0111 0010 1101 10000 - 1101 (-) 0011

## Slide 17: Unsigned Subtraction (continued)
The subtraction, 2n - N, is taking the 2’s complement of N
To do both unsigned addition and unsigned subtraction requires:
Quite complex!
Goal: Shared simpler logic for both addition and subtraction
Introduce complements as an approach

## Slide 18: Complements
Two complements:
  Diminished Radix Complement of N
    (r - 1)’s complement for radix r
    1’s complement for radix 2
    Defined as (rn - 1) - N
  Radix Complement
    r’s complement for radix r
    2’s complement in binary
    Defined as rn - N
Subtraction is done by adding the complement of the subtrahend
If the result is negative, takes its 2’s complement

## Slide 19: Binary 1's Complement
For r = 2, N = 011100112, n = 8 (8 digits):
(rn – 1) = 256 -1 = 25510 or 111111112
The 1's complement of 011100112 is then:
11111111
– 01110011
10001100
Since the 2n – 1 factor consists of all 1's and since 1 – 0 = 1 and 1 – 1 = 0, the one's complement is obtained by complementing each individual bit (bitwise NOT).

## Slide 20: Binary 2's Complement
For r = 2, N = 011100112, n = 8 (8 digits), we have:
(rn ) = 25610 or 1000000002
The 2's complement of 01110011 is then:
100000000 – 01110011 10001101
Note the result is the 1's complement plus 1, a fact that can be used in designing hardware

## Slide 21: Alternate 2’s Complement Method
Given: an n-bit binary number, beginning at the least significant bit and proceeding upward:
  Copy all least significant 0’s
  Copy the first 1
  Complement all bits thereafter.
2’s Complement Example:
  10010100
  Copy underlined bits:
  100
  and complement bits to the left:
  01101100

## Slide 22: Subtraction with 2’s Complement
For n-digit, unsigned numbers M and N, find M  N in base 2:
  Add the 2's complement of the subtrahend N to the minuend M: M + (2n  N) = M  N + 2n
  If M  N, the sum produces end carry rn which is discarded; from above, M - N remains.
  If M < N, the sum does not produce an end carry and, from above, is equal to 2n  ( N  M ), the 2's complement of ( N  M ).
  To obtain the result  (N – M) , take the 2's complement of the sum and place a  to its left.

## Slide 23: Unsigned 2’s Complement Subtraction Example 1
Find 010101002 – 010000112
01010100 01010100
– 01000011 + 10111101
00010001
The carry of 1 indicates that no correction of the result is required.
1
2’s comp

## Slide 24: Unsigned 2’s Complement Subtraction Example 2
Find 010000112 – 010101002
01000011 01000011
– 01010100 + 10101100
11101111
00010001
The carry of 0 indicates that a correction of the result is required.
Result = – (00010001)
0
2’s comp
2’s comp

## Slide 25: Signed Integers
Positive numbers and zero can be represented by unsigned n-digit, radix r numbers. We need a representation for negative numbers.
To represent a sign (+ or –) we need exactly one more bit of information (1 binary digit gives 21 = 2 elements which is exactly what is needed).
Since computers use binary numbers, by convention, the most significant bit is interpreted as a sign bit:
s an–2  a2a1a0 where: s = 0 for Positive numbers s = 1 for Negative numbers and ai = 0 or 1 represent the magnitude in some form.

## Slide 26: Signed Integer Representations
Signed-Magnitude – here the n – 1 digits are interpreted as a positive magnitude.
Signed-Complement – here the digits are interpreted as the rest of the complement of the number. There are two possibilities here:
  Signed 1's Complement
    Uses 1's Complement Arithmetic
  Signed 2's Complement
    Uses 2's Complement Arithmetic

## Slide 27: Signed Integer Representation Example
r =2, n=3
Number
Sign
-
Mag.
1's Comp.
2's Comp.
+3
011
011
011
+2
010
010
010
+1
001
001
001
+0
000
000
000
–
0
100
111
—
–
1
101
110
111
–
2
110
101
110
–
3
111
100
101
–
4
—
—
100

## Slide 28: Signed-Magnitude Arithmetic
If the parity of the three signs is 0:
    1. Add the magnitudes.
    2. Check for overflow (a carry out of the MSB)
    3. The sign of the result is the same as the sign of the first operand.
If the parity of the three signs is 1:
    1. Subtract the second magnitude from the first.
    2. If a borrow occurs:
      take the two’s complement of result
      and make the result sign the complement of the sign of the first operand.
    3. Overflow will never occur.

## Slide 29: Sign-Magnitude Arithmetic Examples
Example 1: 0010 + 0101
Example 2: 0010 + 1101
Example 3: 1010 - 0101
Notes: Example 1: Since the parity of the signs is 0: ADD magnitudes giving 111
Append the sign of the first operand to obtain 0111
Example 2: Since the parity of the signs is 1: SUBTRACT 010
- 101
101 Borrow of 1
Taking the 2’s complement and appending the complement of the sign: 1011
Example 3: Since the parity of the signs is 0, ADD the magnitudes 010
101
111
Appending the sign if the top operand: 1111

## Slide 30: Signed-Complement Arithmetic
Addition:
  1. Add the numbers including the sign bits, discarding a carry out of the sign bits (2's Complement), or using an end-around carry (1's Complement).
  2. If the sign bits were the same for both numbers and the sign of the result is different, an overflow has occurred.
  3. The sign of the result is computed in step 1.
Subtraction:
  Form the complement of the number you are subtracting and follow the rules for addition.

## Slide 31: Signed 2’s Complement Examples
Example 1: 1101 + 0011
Example 2: 1101 - 0011
Notes: Example 1: Result is 0000. The carry out of the MSB is discarded.
Example 2: Complement 0011 to 1101 and add. Result is 1010. The carry out of the MSB is discarded.

## Slide 32: 2’s Complement Adder/Subtractor
Subtraction can be done by addition of the 2's Complement.
1. Complement each bit (1's Complement.)
2. Add 1 to the result.
The circuit shown computes A + B and A – B:
For S = 1, subtract, the 2’s complement of B is formed by using XORs to form the 1’s comp and adding the 1 applied to C0.
For S = 0, add, B is passed through unchanged

## Slide 33: Overflow Detection
Overflow occurs if n + 1 bits are required to contain the result from an n-bit addition or subtraction
Overflow can occur for:
  Addition of two operands with the same sign
  Subtraction of operands with different signs
Signed number overflow cases with correct result sign 0 0 1 1 + 0 - 1 - 0 + 1 0 0 1 1
Detection can be performed by examining the result signs which should match the signs of the top operand

## Slide 34: Overflow Detection
Signed number cases with carries Cn and Cn-1 shown for correct result signs: 0 0 0 0 1 1 1 1
0 0 1 1 + 0 - 1 - 0 + 1 0 0 1 1
Signed number cases with carries shown for erroneous result signs (indicating overflow): 0 1 0 1 1 0 1 0
0 0 1 1 + 0 - 1 -0 + 1 1 1 0 0
Simplest way to implement overflow V = Cn + Cn - 1
This works correctly only if 1’s complement and the addition of the carry in of 1 is used to implement the complementation! Otherwise fails for - 10 ... 0